## Slide 1: Project on LALP (Language for Aggressive Loop Pipelining) CECS 530 Project Proposal
Group 5
Members
Karan Bhandari (c)
Chris Seda Tum
Chinmayi Kambhampati
Rojelio Cruz
Dwarkesh Prassana
Prathima Sidda
Under the aegis and guidance of Dr. Xiaolong Wu
Based on IEEE paper “LALP: A Novel Language to Program Custom FPGA-based Architectures” by Ricardo Menotti et. al

## Slide 2
How?
-LALP uses C like syntax
- Pipelining occurs by specifying clock cycles as directives
- Uses Graphviz as visualization tool
What?
Provides a higher abstraction level than HDLs to exploit parallelism of hardware in FPGAs
Why?
- Hardware Knowledge is needed for reconfigurable devices
- Existing algorithms are high level(HLL)
-HLL cannot replicate hardware, parallelism, DSP

## Slide 3
Is based on two main ideas that were developed for data-driven architectures:
  Dynamic Loop Pipelining
  Pipelining Sequence Loops of Data Dependent Data Loops

## Slide 4: Compilation Flow
Parsing Stage: Takes a program implemented in LALP’s domain specific language and generates a Control and Data Flow Information graph (CDFG)
The ALP performs some analysis and optimization in the graph as well as scheduling
Generates hardware (.vhd file) by selecting components from the existing library

## Slide 5: LALP Limitations
GUI is unstable
Output is error prone
Untested Examples
No procedure calling
Hardware generation library currently has a total of 56 components (no floating point operations)
Only allows simple constructs
No support for resource sharing hardware

## Slide 6: Tasks
Karan Bhandari
- GUI revamping and redoing
- Conceptual code of memory module in ALP
- Test Fibonacci series and max of numbers on the board
- Communicating with the founders, coordination and facilitation
Rojelio Cruz
- Implementing ADPCM
- Conceptual UART module
Chinmayi Kambhampati
Implement and analyze bubble sort and CRC through various stages- ALP, VHDL, Graphviz

## Slide 7
Prathima Sidda
Graphviz- (Test dependencies and resolution in max, Fibonacci)
Chris Seda Tum
Test Algorithms (DFS and Dijkstra)
Dwarkesh Prassana
Performance testing and analysis on Windows and Unix within the realms of two architectures

## Slide 8: In a nut shell – Goals of our project
Implement Fibonacci series and max on the board
Redo and revamp the GUI
Implementing ADPCM Encoder/ Decoder on Atlys Spartan 6 FPGA Development board
Test/Replicate Sample code, Algorithms and Graphviz.
Conceptual UART and memory
Performance analysis

## Slide 9: Progress so far
Commenced working on the GUI
We are in the thick of the knowledge acquisition phase.
We have contacted the founder Ricardo and obtained access to their SVN and code as a committer.

## Slide 10: Questions ?